## Slide 1
Next Generation Communication Server
CS1000
2003.04.23
System Monitoring & Trace

## Slide 2
System Monitoring Command
$ help : available commands display.
$ dir : display the files in DiskOnChip.
$ del file_name : delete the file.
$ ren file_name1 file_name2 : rename the file_name1 to file_name2
$ copy file_name1 file_name2 : copy the file_name1 to file_name2
$ format ds0: DiskOnChip format
$ netcfg -d(c) : display(change) network configuration
$ dm address : display the value of the address.
$ cm address : change the value of the address.
address current_value new_value : change the value
address current_value . : exit to change mode
$ qh *(q_number) : display all kinds of system queue(the queue) status. (Local command, Local event…)
$ qd out_point count q_number : display the queue content from in_point to in_point + count.
$ dqh *(q_number) : display all kinds of disk queue(the queue) status. (fault.dq, pmstx.dq)
$ dqd out_point count q_number : display the disk content from in_point to in_point + count.
$ call : jump to call monitor

## Slide 3
CALL Level Monitoring Command
CALL_MON> help : available commands display.
CALL_MON> ex : return to system monitor.
CALL_MON> cpmver : display the version of active cpm.img.
CALL_MON> vdvid : display the device identification value(device_id).
CALL_MON> tl a(port_no1 port_no2 ) : trace enable for all call message(from the port_no1 to the port_no2 )
tl : trace disable for the trace.
CALL_MON> dv device_id : trace enable for the device.
dv : trace disable for the trace.
CALL_MON> lin port_no : display the port status.
CALL_MON> lis port_no : display the ports status from port_no to port_no + 32.
CALL_MON> itl c(f) : trace enable for ISDN L3 message by complete mode(flow mode).
itl : trace disable for the trace.
CALL_MON> qtl c(f) : trace enable for QSIG L3 message by complete mode(flow mode).
qtl : trace disable for the trace.
CALL_MON> prirst port_no : start PRI RESTART PROCEDURE of the slot including the port_no.

## Slide 4
CALL Level Monitoring Command
CALL_MON> mbwsw : make nailed switch.
CALL_MON> cbwsw : cur nailed switch.
CALL_MON> ex : return to system monitor.
CALL_MON> swm : jump to switch monitor.
CALL_MON> db : jump to data base monitor.

## Slide 5
Switch Monitoring Command
CS-SWM> help : available commands display.
CS-SWM> vgs a(group_no) : display all(group_no) switch matrix.
CS-SWM> msw port_no1 port_2 : make both way switch.
CS-SWM> csw port_no1 port_2 : cut both way switch.
CS-SWM> mrx port_no1 port_2 : make one way switch from port_no2 to port_no1.
CS-SWM> crw port_no1 port_2 : cut one way switch from port_no2 to port_no1.
CS-SWM> gainset dtmf_rx_gain port_rx_gain : set dtmf(0x00 ~ 0x1F) receive gain and ports(0x20 ~ 0x3FF)
receive gain.
CS_SWM> ex : return to call monitor.

## Slide 6
Data Base Monitoring Command
CS-DB> help : available commands display.
CS-DB> dir * : display all data base start address.
dir characters : display the data base start address including the characters.
CS-DB> tb data_base_name[index] : display the data base value by the index.
CS_DB> ex : return to call monitor.

## Slide 7
Reading the Switching status
CS-SWM> vgs 1
0 1 2 3 4 5 6 7 8 9 a b c d e f
#000 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#010 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#020 xxx xxx xxx 040 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#030 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#040 023 xxx xxx xxx xxx xxx xxx 08a xxx xxx xxx xxx xxx xxx xxx xxx
#050 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#060 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#070 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#080 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx 047 xxx xxx xxx xxx xxx
#090 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#0a0 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#0b0 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#0c0 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#0d0 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#0e0 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
#0f0 xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
* system tone port
0x00 ~ 0x0f
* DTMF sender
0x10 ~ 0x1f(TX)
* DTMF Receiver
0x00 ~ 0x2f(RX)
* on conversation
0x23 port and 0x40 port
0x47 port and 0x8a port

## Slide 8
Reading call trace message
[ Format ]
E042 <DE->CA> [0b][12] Off_Hook....... [00/00] 00 01 02 f6 6a 9c 01 02 82 f6 23
E042 <CA->DE> [0b][97] Receive Digits. [00/00] ff ff ff ff ff ff ff ff ff ff 22
Additional Data
Sub State
Main State
Message Description
Message ID
Device ID
Message Direction
Port Number(port_no)
Type of the port_no
* Message Direction :AE(SLT), DE(DTEL), AD(ATD), WT(DECT), W2(DECT2), CO(APTC), RE(ALTC)
DT(DNIC-DTC), MF(DTMF), BS(PRI/BRI), VP(VPM), IP(VOIP), TM(TIMER)
* Type of the port_no : E(Extension), T(Trunk), P(PRI/BRIT/QSIG), B(BRIS)

## Slide 9
Reading ISDN/QSIG L3 trace message
PBX NODE
| |
| Q_SETUP (QT:0122 S:00)|
|--------------------------------------------------->| 00000708 0201b405
| SAPI=00 TEI=00 CRL=02 CR=01b4 | 04038090 a31803a1
| | 83826c06 00813230
| | 30317005 c9313030
| | 30
| |
| I_ALERTING (PT:0081 S:03)|
00000808 02819801 |<---------------------------------------------------|
1803a983 81 | SAPI=00 TEI=00 CRL=02 CR=8198 |
| |
| Q_RELEASE (QT:0122 S:01)|
|--------------------------------------------------->| 00000708 0201b44d
| SAPI=00 TEI=00 CRL=02 CR=01b4 | 08028190

## Slide 10
Special Debug
In case of System Restart
1) connect OMS and capture fault messages
2) connect SIO and execute the following commands and capture.
$ exc
date:2002-01-25,time:09:31:47,counter:f7
exception: address error
pc = 0110f6f4 sr = 2004
usp = 010014ea msp = 00000000 isp = 01fb62f4 vbr = 01000000
sfc = 00000007 dfc = 00000007
d0 = 00000005 d1 = 00000001 d2 = 00000002 d3 = 00000001
d4 = 00000002 d5 = 00000000 d6 = 00000000 d7 = 00000000
a0 = 01fb6414 a1 = 01fb630c a2 = 00000001 a3 = 01fb6404
a4 = 01fb63a0 a5 = 0112de66 a6 = 01fb641c a7 = 01fb62f4
$ CALL_MON>setflag 8 1
Idx=8 : System Last Message Debug : Enable
$ CALL_MON>syslstms
System Last Message Save : PB Event : Len=16
020020118f020000000000000000003c

## Slide 11
Special Debug
In case of System Watch Dog
1) connect OMS and capture fault messages
2) connect SIO and execute the following commands and capture.
$ CALL_MON> lstms
In pointer = 4
No Pno MS SS rel CM CS cpt PB 01 02 DV FC 00 01 02 03 04 05 06 07 08 09 10
================================================================
00 040 01 00 000 ff ff 000 00 00 40 00 90 33 09 98 01 47 8e 88 01 47 81 38
02 ff 16 aa ff ff ff ff ff ff ff ff ff ff ff ff
01 040 01 03 000 ff ff 000 00 00 40 00 90 14 09 98 01 47 8e 88 01 47 81 38
02 ff 16 aa ff ff ff ff ff ff ff ff ff ff ff ff

## Slide 12
Special Debug
In case of Port Blocking
1) connect OMS and capture fault messages
2) connect SIO and execute the following command and capture.
$ CALL_MON> evtms port_n0
Port = 020 In pointer = 0
No MS SS relp CM CS cptr PB 01 02 DV FC 00 01 02 03 04 05 06 07 08 09 10
===============================================================
00 00 00 0000 ff ff 0000 05 00 62 0b 20 01 01 01 18 00 01 00 01 10 00 41
01 00 00 0000 ff ff 0000 00 00 62 00 06 00 00 00 62 00 00 00 00 00 40 01
02 04 00 4001 05 00 0062 05 00 62 0b 12 00 01 01 e6 3e f2 01 97 7c 00 50
03 06 00 4001 06 00 0062 05 00 62 0b 11 00 01 01 e6 3e f2 01 97 7c 00 51
04 00 00 0000 ff ff 0000 05 00 62 0b 12 00 01 0a ca 3e b8 01 0a 8a ca 52
05 02 00 0000 ff ff 0000 05 00 62 0b 14 00 0a 8a ca fe 01 0a 8a 01 00 88
06 02 00 0000 ff ff 0000 05 00 62 0b 15 0a 00 14 00 0a 8a ca fe 01 0a f4
07 02 05 0081 05 00 0062 05 00 62 0b 15 01 00 01 81 ca 3e 14 01 01 81 57
08 02 06 0081 05 00 0062 05 00 62 0b 15 06 00 06 86 ca 3e 14 01 06 86 3e
09 02 06 0081 05 00 0062 05 00 62 0b 15 0a 00 0a 8a ca 3e 14 01 0a 8a 2a
10 02 06 0081 05 00 0062 05 00 62 0b 15 0a 00 0a 8a ca 3e 14 01 0a 8a 2a
11 02 06 0081 05 50 0062 00 00 62 00 0f 00 00 00 00 00 00 00 00 00 00 81
12 02 4b 0081 07 00 0062 00 00 62 00 70 ff ff 00 00 00 00 00 00 00 00 81
13 05 00 0081 07 00 0062 00 00 62 00 90 08 09 98 01 48 07 30 01 47 f7 38
14 05 00 0081 08 00 0062 00 00 62 00 02 81 00 00 00 00 00 00 00 00 00 81
15 06 00 0081 08 00 0062 05 00 62 0b 11 00 01 01 e6 3e f2 01 97 7c 00 51

## Slide 13
Special Debug
In case of VMS Service Fail
1) connect SIO and execute the following command and capture.
$ prt 1e (Enable)
VMS Status(184<-1be) mr=0,sb=11,c=ff,rv=ff,cfwd=000
Auto ATD Svc(0184) cause=9b
VMS DTMF Sending Info(vms_pno 0184, send_buf[b2 a1 5f ff ff ff]
$ prt 0 (Disable)
In case of SMDA Service Fail
$ prt 18 (Enable)
[SMDA Result:Serial_NO(0000)]---------------------------------------------------
Current Time : 2002/01/28 05:30:10
Use Telno : 1aa1ff Used Line : 0084
Out Digit(Local:2)=1aaa
Start Time : 2002/01/28 05:30:02 End Time : 2002/01/28 05:30:10
Metering Units = 13
$ prt 0 (Disable)
$ dqh 0
# Fname = pmstx.dq in-p = 1 out-p = 0 64 * 2710 : PMS TX